## Slide 1: Camera and Projection
Slide courtesy: S. Lazebnik, S. Savarese, M. Brown

## Slide 3: Camera obscura
Leonardo da Vinci (1452-1519): first record of camera obscura
"When images of illuminated objects ... penetrate through a small hole into a very dark room ... you will see [on the opposite wall] these objects in their proper form and color, reduced in size ... in a reversed position, owing to the intersection of the rays".
-- Da Vinci

## Slide 4: Birth of photography
Joseph Nicephore Niepce (1822): first photo - birth of photography
Photography (Niepce, “La Table Servie,” 1822)

## Slide 8: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction(衍射) effects…
Slide by Steve Seitz

## Slide 9: Shrinking the aperture

## Slide 10: The reasons for lenses
The main reason for using a lens is to keep the picture in sharp focus while gathering light from a large area.

## Slide 11: Adding a lens
Slide by Steve Seitz
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)

## Slide 12: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
    All parallel rays converge to one point on a plane located at the focal length f
Slide by Steve Seitz
focal point
f

## Slide 13: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
“circle of
confusion”
Slide by Steve Seitz

## Slide 14: Thin lens formula
What is the relation between the focal length ( f ), the distance of the object from the optical center (D), and the distance at which the object will be in focus (D′)?
f
D
D′
Slide by Frédo Durand
object
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 15: Thin lens formula
f
D
D′
Similar triangles everywhere!
Slide by Frédo Durand
object
image plane
lens

## Slide 16: Thin lens formula
f
D
D′
Similar triangles everywhere!
y′
y
y′/y = D′/D
Slide by Frédo Durand
object
image plane
lens

## Slide 17: Thin lens formula
f
D
D′
Similar triangles everywhere!
y′
y
y′/y = (D′−f )/f
Slide by Frédo Durand
object
image plane
lens
y′/y = D′/D

## Slide 18: Thin lens formula
f
D
D′
1
D′
D
1
1
f
+
=
Any point satisfying the thin lens equation is in focus.
Slide by Frédo Durand
object
image plane
lens
Notes: And the set of all such points forms a plane parallel to the image (plane of focus).
Uses of the formula: given focal length and depth in scene that you want to be in focus, it tells you where to put the image plane. Given f and distance of image plane from camera center, it tells you which depth in the scene will be in focus.

## Slide 19: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm
Slide by A. Efros
Notes: Depth of field is the distance between the nearest and farthest objects in a scene that appear acceptably sharp in an image (Wikipedia)

## Slide 20: Controlling depth of field
http://en.wikipedia.org/wiki/File:Depth_of_field_illustration.svg
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure

## Slide 21: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide by A. Efros

## Slide 22: Field of view (FOV)
Wide-angle lens(广角镜头): when the focal length is (much) shorter than the effective diameter of the retina
Telephoto lens(长焦镜头): have a small field of view and produce pictures closer to affine ones
Field of view: portion of scene space that actually projects onto the retina of the camera
Determined by the focal length and the effective area of the retina (or CCD, film, etc)
  d - the effective diameter of the sensor/lens
  f - focal length
  f/d - f number
  FOV - 2φ

## Slide 23: Field of View
Slide by A. Efros
Notes: The field of view is the angular extent of the world that is observed by the camera.

## Slide 24: Field of View
Slide by A. Efros

## Slide 25: Field of View / Focal Length
Large FOV, small f
Camera close to car
Small FOV, large f
Camera far from the car
Sources: A. Efros, F. Durand

## Slide 26: Same effect for faces
standard
wide-angle
telephoto
Source: F. Durand

## Slide 27: Exposure = aperture + shutter speed
Aperture of diameter D restricts the range of rays (aperture may be on either side of the lens)
Shutter speed is the amount of time that light is allowed to pass through the aperture
F

## Slide 28: Exposure
Two main parameters:
  Aperture (in f stop)
  Shutter speed (in fraction of a second)

## Slide 29: Effects of shutter speeds
Slower shutter speed => more light, but more motion blur
Faster shutter speed freezes motion
1/125
1/250
1/500
1/1000
Walking people
Running people
Car
Fast train
From Photography, London et al.

## Slide 30: Aperture
Aperture is the diameter of the lens opening, usually specified by f-stop, f/D, a fraction of the focal length.
  f/2.0 on a 50mm means that the aperture is 25mm
  f/2.0 on a 100mm means that the aperture is 50mm
When a change in f-stop occurs, the light is either doubled or cut in half.
Lower f-stop, more light (larger lens opening)
Higher f-stop, less light (smaller lens opening)
Notes: http://www.uscoles.com/fstop.htm
1.4 2.0 2.8 4 5.6 8 11 16 22

## Slide 31: In-camera Imaging Pipeline

## Slide 38
Bayer RGB pattern: (a) color filter array layout; (b) interpolated pixel values, with unknown (guessed) values shown as lower case.

## Slide 47: Geometry Camera Models

## Slide 48: Geometry Camera Models
Establish quantitative constraints between measurements made in an image and the position and orientation of geometric figures measured in some external coordinate system.
  analytical Euclidean geometry
  intrinsic parameters
  extrinsic parameters

## Slide 84: Summary
Mapping between image and world coordinates
  Pinhole camera model
  Projective geometry
  Projection matrix

## Slide 85
Camera Calibration